## Slide 1
Migrating FDOT Projects from SS10 to OpenRoads Designer
Presented By: Christiana Holmes

## Slide 2
Overview of Steps for Migrating Projects
Steps:
Upgrade all files to SS10.
Clean up MicroStation data in FDOT SS10 WorkSpace.
Clean up Civil data in FDOT SS10 WorkSpace.
Upgrade files from SS10 to OpenRoads.
Remap Feature Definitions in DGN files.
Upgrade and Remap Feature Definitions in Template Library.
Clean up Migrated/Remapped OpenRoads DGN files.

## Slide 3
Things to consider when Migrating Projects
The DGN Files MUST be in the SS10 version.
Survey Features CANNOT be remapped.
Drainage Features CANNOT be remapped.
Surface Templates will need to have a Feature Definition set manually.
May need to drop Civil Cells to properly remap feature definitions.
If changes need to be made to the Superelevation calculations, the Super will need to be recreated and reassigned to the Corridor. The existing Superelevation point controls will need to be removed from the corridor.
If changes are made to the Alignment, sheets will need to be recreated.
Horizontal Feature Constraints will need to be reset (in the ITL) to the updated Feature Definition and may need to be re-assigned to the Corridor.

## Slide 4
Step 1:
Upgrade all Project files to SS10.
Step 2:
The dgn files need to be as “Clean” as possible before migrating them to OpenRoads.
Cleaning the files should be done in SS10 and in the FDOT WorkSpace.
To Clean Up the MicroStation Data key-in commands should be ran on the Project files:
  Fix Range
    Key-in: mdl load fixrange
  Verify DGN
      Key-in: mdl load verifydgn; verifydgn repair
  Compress File
    Key-in: compress design
  Save Settings
    Key-in: file design
NOTE: This should be done on EVERY .dgn file in the Project and can be done in batch process.
Step 1 & 2: Upgrading to SS10/Clean up MicroStation Data

## Slide 5
DEMO!!
Step 1 & 2: Upgrading to SS10/Clean up MicroStation Data

## Slide 6
Step 1 & 2: Upgrading to SS10/Clean up MicroStation Data

## Slide 7
Step 3: Clean up Civil Data
Step 3:
Open ALL Corridor files and ensure the Corridors are ACTIVE.
Remove any unnecessary data from files. Example, remove Survey Settings from all models in all files (except Survey, Terrains).

## Slide 8
Step 3: Clean up Civil Data
Step 3:
Open each model of each file and run the Key-in: Civil Display Browser.
Select the Repair Relationships button to clean up civil relationships.
NOTE: Run this on ALL files with Civil Data and do this in order of dependency (i.e. Survey, Terrains, Alignments, Corridors, etc.).

## Slide 9
DEMO!!
Step 3: Clean up Civil Data

## Slide 10
Step 3: Clean up Civil Data

## Slide 11
Step 4:
Launch Civil File Manager. This tool can be opened inside or outside of OpenRoads.
  Outside ORD: Path to the executable is C:\Program Files\Bentley\OpenRoads Designer CE xx.xx\OpenRoadsDesigner\CivilFileManager.exe
  Inside ORD: File > Civil Tools > Civil File Manager
In the Civil File Manager dialog, select File > Open > Folder + sub folders and navigate to the project folder location.
Step 4: Upgrade Files from SS10 to ORD

## Slide 12
Step 4:
The project folder and subfolders will load in the left window of the dialog.
In the Civil File Manager dialog, select Action > Upgrade All (Force). The files will process and be upgraded to ORD CE.
NOTE: Upgrades only have to be done on files that have civil data.
Step 4: Upgrade Files from SS10 to ORD

## Slide 13
DEMO!!
Step 4: Upgrade Files from SS10 to ORD

## Slide 14
Step 4: Upgrade Files from SS10 to ORD

## Slide 15
Step 5:
Open each of the civil files in OpenRoads in order of dependency (i.e. Survey, Terrains, Alignments, Corridors, etc.). Each file will be associated with the WorkSpace/WorkSet.
Check the files and ensure they were properly updated.
  Geometry Files: Check to make sure the correct Terrain is set as active.
  Corridor Files: (1) Check that each Corridor is Active (2) Reset the Active Terrain.
Step 5: Remap Feature Definitions in DGN Files

## Slide 16
Step 5:
Run the Civil Feature Remapper on each Civil File.
  File > Civil Tools > Civil Feature Remapper
  Set the path for the Remapper XML file that is getting created.
  Create a New Remapping Configuration XML file that points to the FDOT Remapping Spreadsheet.
  Remap the Active DGN Features.
  NOTE: Remapping files can be done as a batch process.
Step 5: Remap Feature Definitions in DGN Files

## Slide 17
DEMO!!
Step 5: Remap Feature Definitions in DGN Files

## Slide 18
Step 5: Remap Feature Definitions in DGN Files

## Slide 19
Step 6:
In one of the Project Corridor Files, open the project Template Library.
  NOTE: Opening the ITL file in OpenRoads will upgrade the file to the current version.
Close the ITL file and click Yes to SAVE the ITL file.
Open a “dummy” ITL file.
  NOTE: The ITL that you are remapping CANNOT be the active/open ITL for the features to remap.
Step 6: Upgrade and Remap Feature Definitions in Template Library

## Slide 20
Step 6:
Run the Civil Feature Remapper on the ITL File.
  File > Civil Tools > Civil Feature Remapper
  Set the path for the Remapper XML file that is getting created.
  Create a New Remapping Configuration XML file that points to the FDOT Remapping Spreadsheet.
  Remap the ITL file Features.
    NOTE: Horizontal Feature constraints will need be reset to the updated Feature Definitions.
Step 6: Upgrade and Remap Feature Definitions in Template Library

## Slide 21
Step 6:
Re-synchronize the corridors with the updated ITL.
Check that the Corridors are using the updated Feature Definitions using the Component Quantities Report.
Step 6: Upgrade and Remap Feature Definitions in Template Library

## Slide 22
DEMO!!
Step 6: Upgrade and Remap Feature Definitions in Template Library

## Slide 23
Step 6: Upgrade and Remap Feature Definitions in Template Library

## Slide 24
Step 7:
In the Corridor Files, run the Civil Display Browser key-in and toggle on Show Object Checking to view issues that may persist in the Civil Data.
Re-synchronize all templates for all Corridors and Linear Templates.
Set a Feature Definition for all Surface Templates. This must be done from the 3D view and from the context menu.
Process all Corridors
Run Component Quantities on the corridors to make sure the component features have been remapped properly
Delete the old Feature Definitions and Feature Symbologies from Explorer.
Delete old Element Templates.
Step 7: Final Cleanup

## Slide 25
DEMO!!
Step 7: Upgrade and Remap Feature Definitions in Template Library

## Slide 26
Step 7: Upgrade and Remap Feature Definitions in Template Library

## Slide 27
Help with Project Migration!
ITL Feature Remapper:
https://communities.bentley.com/products/road___site_design/w/road_and_site_design__wiki/48316/video-template-library-itl-feature-remapper
  Civil File Manager:
  https://communities.bentley.com/products/road___site_design/w/road_and_site_design__wiki/51913/civil-file-manager
Project Migration:
  https://communities.bentley.com/products/road___site_design/w/road_and_site_design__wiki/51285/migrating-project-data-to-openroads-designer

## Slide 28
Thank You!