## Slide 1
Limited Access Incentive & Disincentive
Project Summary

## Slide 2: Original Interstate Data 2005 to 2010
Chart: International Roughness Index (inch/mile)
 | 0 | 5
 | 0 | 5
 | 0 | 5
Incentive Zone:
IRI≤42
36% of LOTs
Full Pay Zone:
43≤IRI≤55
40% of LOTs
Disincentive Zone:
56≤IRI≤95
23% of LOTs
Remove & Replace Zone:
IRI>95
0.6% of LOTs
IRI STATISTICS
Central Tendency:
Average: 48
Median: 47
Dispersion:
Range: 126
Std Dev: 13

## Slide 3: 2019 & 2020 Limited Access IRI Projects
Chart: International Roughness Index (inch/mile)
 | 0 | 5
 | 0 | 5
 | 0 | 5
IRI STATISTICS
2005-2010
Avg: 48 in/mile
2018-2019
Avg: 43 in/mile

## Slide 4: IRI Improvement on Limited Access Roadways
Chart: 
IRI Incentive/Disincentive | 63.3598 | 58.8662 | 59.9684 | 58.8977 | 56.5337 | 54.5108 | 48.0228 | 48.5582 | 48.1848 | 47.1137 | 47.1558 | 46.4303 | 45.9523 | 43.869 | 43.4343 | 45.7481 | 43.1158 | 43.7104 | 43.0427 | 42.075 | 41.1024 | 40.3458 | 40.3307 | 39.5903 | 39.1704 | 39.5987 | 39.3146 | 38.6579 | 39.2538 | 38.4123 | 38.2342 | 37.9594 | 37.9112 | 37.5474 | 36.944 | 36.7034 | 36.8 | 36.3106 | 36.221 | 35.3204 | 34.7504 | 34.6602 | 34.359 | 34.1073 | 33.946 | 31.5652 | 31.2596 | 24.1971

## Slide 5: IRI Incentive/Disincentive Project Overview
47 projects from 2013 through Nov 2020
  Min project IRI = 24 in/mile, max project IRI = 63 in/mile
  38 projects received an incentive
  Four projects qualified for a consistency bonus (all LOTs ≤ 55 in/mile)
  Avg pay adjustment is $700 per mile

## Slide 6: IRI Incentive/Disincentive Project Overview
Six projects in 2019
  Min Project IRI = 38 in/mile, Max Project IRI = 60 in/mile
  Five projects received an incentive
  No projects received a consistency bonus
  Avg pay adjustment was $355 per mile

## Slide 7: IRI Incentive/Disincentive Project Overview
Eight projects in 2020 (through Nov)
  Min project IRI = 24 in/mile, max project IRI = 55 in/mile
  Seven projects received an incentive
  One project qualified for a consistency bonus
  Avg pay adjustment is $1050 per mile