## Slide 2: Context Class Capacity Integration into Travel Demand Models
Govardhan Muthyalagari, PE, PTOE

## Slide 3
Overview
Need for travel demand model updates
Complete Streets 360°
(FDOT Context Classification Framework)
Objective
Methodology
Findings
Next Steps
3

## Slide 4: Value in Updating Travel Demand Modeling
Accurate Future Projections:
Changing Demographics
Economic Shifts
Technological Advancements
Informed
Decision-Making:
Investment Prioritization
Policy Development
Emergency Planning
Improved Environmental Impact Assessments:
Emissions Reduction
Land Use Planning
Adapting to Changing Conditions:
Real-time Updates
Scenario Analysis
4
Notes: Travel demand models are valuable because they use trusted data sources such as the US Census Bureau, Federal Highway Administration, Bureau of Transportation Statistics, Florida DOT, and local governments.
The models rely on processes developed, tested, and improved over the last 60 years to provide reasonably reliable insights into future traffic volumes that supports transportation decision-making.
Planners often forecast short-term traffic using recent trends, but this method becomes unreliable beyond five years. Traffic growth slows as it approaches the roadway’s capacity, making long-term projections less accurate.Travel demand models, on the other hand, account for the complex traffic diversion caused by congestion, or the spillover effect of traffic diverting to other facilities in the transportation network.
Models account for land use changes expected over the next 20-30 years. These changes in development may significantly alter travel patterns.

## Slide 5: COMPLETE STREETS 3600: FDOT CONTEXT CLASSIFICATION FRAMEWORK)
    “Putting the right street in the right place”
    Target Zero
    Safe Systems Approach
  APPROACH
Safe System Approach
5

## Slide 6
FDOT Context Classification Framework
  Roadway characteristics,
  Traffic Patterns, and
  Development Densities within Spatial Context
6

## Slide 7: Objective
Establish a framework for incorporating FDOT's latest Context Class capacity guidelines into travel demand models to improve the accuracy and reliability of future transportation planning and decision-making.
7

## Slide 8: Current Practice
  Area Type (Core Urbanized, Urbanized, Transitioning, Rural)
  Facility Type (Limited Access, Arterial)
  UROAD factor (accounting for roadway geometry)
  CONFAC factor (similar to K factor, accounting for development density)
  Bureau of Public Roads (BPR) Coefficient and Exponent (used in speed-flow relationships)
8

## Slide 9: Next Steps
  National Scan
  Model Selection Criteria
  Implement the Context Class Based Capacities
  Comparison with Key Metrics
  Key Findings
9
Methodology

## Slide 10: Model Selection Criteria
  Tampa Bay Regional Planning Model (TBRPM) was selected
  Accommodates Time-of-day (TOD) and daily volume within the model.
  Coverage of all context classes within the model area's roadway network.
  Requires minimal data and effort for integration of context-based capacities.
  Offers balance between model size and computational efficiency.
10

## Slide 11
  Utilize 2023 FDOT Multimodal Quality/LOS Handbook
  No capacity changes to the limited access facilities
  Updated capacities for State Roadways (C1, C2, C3R, C3C, C4, C5, and C6)
  No capacity changes to the local roadway
Implementation of Context Class Capacities
11

## Slide 12
  Updated speed and capacities based on Context Class - Procedure 15 within Visum model (Python Script File: 2_update_speed_capacity.py)
  5,004 (20%) out of 24,780 links were updated for the 2015 Base Year TBRPM
  Quality check performed for speed and capacity using context classification
12
Implementation of Context Class Capacities

## Slide 13
Compared to 2013 FDOT Q/LOS handbook, the 2023 FDOT Q/LOS handbook shows:
  Reduction in capacities for most of the state roadway context classes
  Increase in capacities for limited access facilities for Urban Core, Urban, Transitioning and Rural Area Types
Trip lengths during peak period all Trip purposes are increased by approx. 1.3%
Higher changes approx. 3.7% increase is observed for the off-peak period for all Trip purposes
TRIP PURPOSE | PEAK - Total Trip Length (Miles) | OFF-PEAK - Total Trip Length (Miles)
HBW | -1.24% | -4.77%
HBSH | -1.54% | -3.38%
HBSR | -1.81% | -2.75%
HBSC | -1.26% | -4.76%
HBO | -1.39% | -2.47%
NHBW | -1.59% | -8.01%
NHBO | -1.61% | -8.28%
LTRK | -1.68% | -6.95%
HTRK | -0.59% | -0.90%
TAXI | -1.95% | -7.15%
EI | 0.64% | 3.54%
AIRP | -0.14% | 0.52%
COL | -0.94% | -4.46%
Overall | -1.28% | -3.67%
Person | -1.39% | -4.32%
Vehicle | -0.05% | 0.99%
13
Findings

## Slide 14: Findings
Overall deviation of around 4% based on the Volume/Count ratio
Traffic volumes have decreased along:
  Freeway/limited access facilities,
  Toll facilities, and
  Collectors
Traffic volumes have increased along:
  Undivided arterials,
  Divided arterials, and
  One Way facilities
Highway Validation by Facility Type |  |  | 
Facility Type | Count | Volume | Volume/Count
Freeway | 0.00% | 4.18% | 3.96%
Divided Arterial | 0.00% | -6.82% | -7.00%
Undivided Arterial | 0.00% | -20.00% | -19.59%
Collector | 0.00% | 1.99% | 1.20%
One Way Facility | 0.00% | -13.04% | -13.28%
Ramps | 0.00% | 5.32% | 5.71%
Toll Facilities | 0.00% | 4.38% | 4.65%
Overall | 0.00% | -3.76% | -4.08%
14

## Slide 15: Next Steps
Evaluate the model outputs showing shift in traffic to arterials.
Explore eliminating or adjusting UROAD/CONFAC in VFACTORS to refine capacities in the Context Class Speed Capacity file.
Compare results within a subarea to understand effects at granular level.
Need to convert LA facilities ( FT 10-19, 70-99) into Urban Core, Urban, Transitioning and Rural Area Types to match the 2023 FDOT Q/LOS handbook.
Need standard guidance to be used by local agencies to reclassify the local roadways with the appropriate context classes.
15

## Slide 16: High-Resolution Statewide Socio-demographic, Land Use and Economic Development Framework for Transportation Planning
Naveen Eluru
Professor in Civil, Environmental and Construction Engineering
University of Central Florida
BOLDLY GOING: TRIPS IN CONTEXT, TFF 2024

## Slide 17: Presentation Outline
Project Vision and Approach
Takeaways
Project Findings
Data products and Use cases

## Slide 18: Background
The project focuses on developing a standardized high resolution state-wide sociodemographic, land use and economic development model
The project will generate a universal template of variables that will be useful for the statewide framework
For the universal template built, the research team will generate socio-economic, land use and economic development variables

## Slide 19: Objectives
To establish a universal template of socio-demographic, land use and economic indicators
To develop and validate an algorithm to generate socio-demographic, land use and economic indicators
To employ the validated algorithm developed to generate future socio-demographic, land use and economic indicators in 5-year increments from 2025 through 2050
To generate the variables for a spatial resolution that can be directly employed for local jurisdictions and statewide models

## Slide 20: Research Overview
Review and stakeholder survey
Data compilation and processing
Conceptualization of the framework
Model estimation
Software development
Validation and consistency checks

## Slide 21
Florida Department of Revenue
U.S. Census Bureau
FDOT Roadway Characteristics Inventory and Florida Geographic Data Library
American Community Survey
UF Population Data
Parcels
Block Group
Census Tract
County
Spatial
Resolutions
Data
Resources

## Slide 22: Conceptual Framework for Land Use Evolution

## Slide 23: Model Framework
Parcel Data with Updated Land Use
Existing Land Use of Parcels
Demographics
BG Level Land Use
Economic Variables
Proposed LU Model Framework

## Slide 24: Land Use Model Structure

## Slide 25
Population
Ethnicity Distribution
Number of HHs
Vehicle Ownership
Number of Jobs
Median Income
Jobs by industry
Number of Businesses
Economic Development Variables
Socio-Demographic
Variables

## Slide 26: Simulation Validation and Results

## Slide 27: Simulation Engine
Land Use Modeling
  LU Change (Binary Logit)
  Parcel Split (Binary Logit)
  Split Fraction (Fractional Split)
  New Land Use (MNL)
Economic & Demographic Modeling
  Population (Linear Regression)
  Race (MNL Fractional Split)
  Vehicle Ownership (MNL Fractional Split)
  Jobs (Linear Regression)
  Income (Linear Regression)
  Jobs by Industry (MNL Fractional Split)
Output
  Updated parcel land use and area
  Updated independent variables
Inputs
  2020 Data
  Models

## Slide 28: Simulation Engine Validation
Chart: 2020 Parcel Land Use Change
| Agricultural | Commercial | Industrial | Institutional | Mixed Use | MF Residential | Office | Other Residential | Others | Public | Recreational | SF Residential | Vacant Commercial | Vacant Industrial | Vacant Institutional | Vacant Public | Vacant Residential | Water
Actual | 0.031 | 0.037 | 0.038 | 0.061 | 0.079 | 0.037 | 0.061 | 0.024 | 0.074 | 0.04 | 0.081 | 0.014 | 0.067 | 0.065 | 0.146 | 0.04 | 0.065 | 0.073
Forecast | 0.033 | 0.035 | 0.035 | 0.07 | 0.076 | 0.031 | 0.059 | 0.023 | 0.074 | 0.034 | 0.067 | 0.013 | 0.077 | 0.064 | 0.147 | 0.04 | 0.07 | 0.073

## Slide 29: Land Use at the State Level
Chart: % of area
| Mixed Use | Vacant Institutional | Vacant Industrial | Office | MF Residential | Industrial | Vacant Commercial
2020 | 0.00052692 | 0.0016268 | 0.0015158 | 0.001884 | 0.004346 | 0.0055335 | 0.0047215
2025 | 0.00061796 | 0.0014032 | 0.0016338 | 0.001978 | 0.0048093 | 0.0057974 | 0.0056108
2030 | 0.00072075 | 0.0014386 | 0.0016972 | 0.0020705 | 0.0052487 | 0.0060946 | 0.0061605
2035 | 0.00081175 | 0.001387 | 0.0018181 | 0.0021825 | 0.005776 | 0.006473 | 0.0067568
2040 | 0.00089652 | 0.0013386 | 0.0020563 | 0.0022763 | 0.006388 | 0.006887 | 0.0072796
2045 | 0.00097372 | 0.0013333 | 0.0023052 | 0.0025376 | 0.0069181 | 0.0072911 | 0.0076262
2050 | 0.0010117 | 0.0013302 | 0.0024986 | 0.002729 | 0.0075568 | 0.007647 | 0.0080179
Chart: % of area
| Recreational | SF Residential | Others | Vacant Public | Public | Agricultural
2020 | 0.061175 | 0.066963 | 0.065231 | 0.10756 | 0.13498 | 0.43685
2025 | 0.058369 | 0.072499 | 0.073311 | 0.10838 | 0.13825 | 0.41578
2030 | 0.055718 | 0.077985 | 0.080729 | 0.10918 | 0.14144 | 0.39483
2035 | 0.053923 | 0.083502 | 0.088561 | 0.11003 | 0.1438 | 0.37339
2040 | 0.052722 | 0.089144 | 0.096543 | 0.11117 | 0.1458 | 0.35138
2045 | 0.051518 | 0.0949 | 0.10397 | 0.11244 | 0.14821 | 0.32991
2050 | 0.050886 | 0.10067 | 0.11129 | 0.1134 | 0.14992 | 0.30862
Chart: % of area
| Water | Commercial | Institutional | Other Residential | Vacant Residential
2020 | 0.012691 | 0.012321 | 0.019763 | 0.029924 | 0.032392
2025 | 0.012803 | 0.012687 | 0.019462 | 0.030979 | 0.035625
2030 | 0.012783 | 0.013186 | 0.019471 | 0.032421 | 0.038821
2035 | 0.010902 | 0.013677 | 0.019463 | 0.035531 | 0.042023
2040 | 0.010937 | 0.014146 | 0.019325 | 0.036658 | 0.045054
2045 | 0.01091 | 0.014587 | 0.01902 | 0.037601 | 0.047947
2050 | 0.010936 | 0.015028 | 0.018856 | 0.03908 | 0.050524

## Slide 30: Data Products

## Slide 31: Parcel Data Sample
Parcel Level Land Use Forecast for 2025

## Slide 32: Block Group Data Sample
Block Group Population Forecast for 2025

## Slide 33: Census Tract Data Sample
Census Tract Median Income Forecast for 2025

## Slide 34: How Can the Data Products Be Used?

## Slide 35: Use Case 1
Every urban/rural jurisdiction in Florida can readily use the data developed for
  Running travel demand models with a universal template of variables
  Jurisdictions can examine future growth generators and types of land use changes
  Explore opportunities to influence patterns to grow their revenue (from tax and business)
Direct consideration in travel demand models as land use variables at different spatial resolutions (BG, CT and county)

## Slide 36: Use Case 2
Use the data products to study how land use patterns are likely to evolve and identify transportation needs
  Increasing residential (such as single-family parcels) will require different infrastructure relative to commercial establishments
Explore how current transportation infrastructure is performing in locations with similar patterns right now and plan proactively for the future
Identify locations where land use patterns are changing significantly and evaluate future transportation infrastructure needs

## Slide 37: Use Case 3
Pro-active safety planning will be possible with the data products
We can use the data products to identify future locations that have a land use pattern that corresponds to high crashes currently
  Proactively plan and apply these corrective measures for these locations that can allow us to avoid re-design or retrofitting
Explore what patterns contribute to safety and pro-actively apply these for different locations based on their evolutionary paths
Proactively examine how land use needs impact safety – study current locations with similar land use and their safety needs and plan for future developments.

## Slide 38: Takeaways
We are building a standard sociodemographic, land use and economic indicator framework for Florida
Land use changes at the parcel level in open-source software that can be aggregated at any resolution including BG, CT and county for ready adoption in Florida
Several potential Use cases are identified for future adoption of these data products
The data presented should be available for all of you to use in 2-3 months

## Slide 39: Acknowledgements
Team Members
  Sudipta Tirtha
  Lauren Hoover
  Md Istiak Jahan
  Dewan Parvez
  Susmita Sarker
Others
  Sheldon Harrison
  Krishnan Viswanathan
FDOT personnel
  Thomas Hill (program manager and main advocate)
  Vladimir Majano
  Terry Corkery

## Slide 40: Questions?
For more details - https://people.cecs.ucf.edu/neluru/
Email: naveen.eluru@ucf.edu

## Slide 41: Freight Discussion
Jeanette Berk

## Slide 42: MentiMeter Instructions (Live Poll)
Welcome to the Live Poll!
Scan the QR Code with your phone to access the questions. Your answers will show up on the screen.
We look forward to hearing your thoughts!

## Slide 47: Thank you for attending!